# MAE 370 laboratory section (9)
# Laboratory (4): Stress Concentration
# Experiment conducted: (2016-11-11)
# Report submitted: (2016-11-18)
# Author:
Cory Wolfe
Group: C

# I) Procedure
First the flexor frame was set up. This involved backing the loading screw out and inserting and clamping down the beam into the frame. Then the beam's dimensions are recorded for use in later calculations. Then the gage's wires are attached to the frame, then the flexor is attached to the strain gage according to the wiring diagrams in the manual. Then the gage is appropriately set to the correct gage factor and the gage is zeroed out to the initial condition of gage one.
Then the initial condition is recorded for the remaining three gages. After this has been completed loading screw is applied until a strain of 2000 microstrains is reported by the gage. After this has been completed the final reading for the remaining gages is recorded. Then the loading screw is removed and the gage was checked for a value of approximately zero.
Items used:
- Flexure frame
- Aluminum beam
- Strain Indicators
- Strain Gage
- Calipers

Equations:
E_{ 4_corrected } = 2000* { S_g1 }over { S_g4 }	(eqn 1)
C = 5.86( %epsilon_1-%epsilon_2)-5.44(%epsilon_2-%epsilon_3 )	(eqn 2)
B = 3.49( %epsilon_1-%epsilon_2 ) - 1.20C	(eqn 3)
A = %epsilon_1 = .743B - .552C	(eqn 4)
%epsilon_{ B_maximum } = A+B+C	(eqn 5)
K_t = { %epsilon_{B_max} } over { %epsilon_{4_corrected} }	(eqn 6)
DO THIS	(eqn 7)
ε in με
Schematics:

# II) Data Summary
Gage	Initial Reading (με)	Final Reading
1	0	2385
2	-676	1346
3	-368	1455
4	-1498	502

b	1.006 in	Sg1	2.08
t	.25 in	Sg2	2.08
x	3.25 in	Sg3	2.08
L	10in	Sg3	2.11
d	.25

III)	Calculations (25 pts)

IV)	Comparison and Discussion (25 pts)
The calculated values for this experiment have an error around eighteen percent. This is slightly higher than the accepted variation. Possible sources of error in this experiment include variations in the strain gage. In addition to this there is a possibility that the final values were changed due to the torsion the screw applied to the beam. This would lead to a variation in the strain applied to the gages. In addition, there were some measurement variance along different portions of the beam, which would lead ot other variations in stress concentration, not limited to the hole.
Table 1: Standard material properties [2]
Material	Material Properties	Used in Laboratories:
Aluminum / (2024-T6)	E = 10.4x106 psi / ν = 0.31	2, 3, and 4
Aluminum / (6061-T651)	E = 10 Msi / σy = 40 ksi / σu = 45 ksi / σb : no standard value / G = 3770 ksi / τprop = 22 ksi	5 and 7
Steel / (1018)	E = 29.7 Msi / σy = 53.7 ksi / σu = 63.8 ksi / σb : no standard value / G = 11.6 Msi / τprop = 31 ksi	5 and 7
Steel (unspecified)	E = 30x106 psi	6 and 8

# V) References and Appendix (5 points)
Gilbert, J. A., Carmen, C. L., Thota, J., MAE/CE 370 - MECHANICS OF MATERIALS - LABORATORY MANUAL, Version 3.0, (2015)

1. MatWeb, http://www.matweb.com, accessed: 8/31/2016.
2. Simple bending plot, available on Canvas.
Appendix A: Units and conversions
Property	English unit(s)	Metric unit(s)
Width, thickness, length, deflection	in, ft	m, cm, mm
Angle	°, radians	°, radians
Percent error	%	%
Area	in2, ft2	m2, cm2, mm2
Moment of Inertia	in4, ft4	m4, cm4, mm4
Force, Load, Weight	lb	N
Torque	in-lb, lb-in	N-m
Stress (normal, shear)	lb/in2 (psi)	N/m2 (Pa)
Modulus of Elasticity / a.k.a. Young’s Modulus E	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Modulus of Rigidity / a.k.a. Shear Modulus G	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Poisson’s Ratio ν	unitless	unitless
Stress Concentration Factor K	unitless	unitless
Strain (normal, shear)	in/in, µε / µε=10-6 in/in	m/m, µε / µε=10-6 m/m

1 ksi	1000 psi
1 in	25.4 mm
1 lb	4.448 N, 453.6 g