# MAE 370 laboratory section (9)
# Laboratory (1): Laboratory report format and useful information
# Experiment conducted: (2016-09-16)
# Report submitted: (2016-09-23)
# Author:
Cory Wolfe
Group:

# I) Procedure
The test apparatus was a combination of the Flexor, for applying a load to the beam, and the strain indicator, to measure the strain on the beam. The strain on the beam was measured by appropriately placed and oriented strain gages on either side of the aluminum beam. A rough schematic is provided at the end of the procedure section. The procdures discussed here come from section 7.4 of the provided MAE 370 Lab Manual.
In order to complete the experiment the group began by recording the gage factor and transverse sensitivity listed on the aluminum beam provided for the experiment. Then the beam was placed in the Flexor, with the longitudinal gage on the upper surface and the gaged end into the clamp.
Then the cables were appropriately ran from the Flexor to the strain indicator. The gage factor was input into the strain indicator where appropriate. Initially the longitudinal measurement was taken with no force applied to zero out the strain indicator. Then the lateral measurment was recorded at the longitudinal strain of zero. Then the loading screw was turned counter-clockwise in order to produce an additional lateral strain of -500 με. Once this value was reached the strain indicator was turned off and the lead for longitudinal strain gage was inserted. The value for longitudinal gage was recorded.
Then the loading screw was removed from the beam in order to check for stability of the system. Since the value was ±10 με the recorded values were usable, since the system was relatively stable.

Items used:
- Aluminum beam
- Flexor
- Strain indicator (incapable of displaying numbers greater than 1999)

%varepsilon _{longitudinal} = %varepsilon _{longitudinal(deflected)} - %varepsilon _{longitudinal(undeflected)} (eqn 1)
%upsilon = {%varepsilon _{lateral}} over { %varepsilon_{longitudinal} }	(eqn 2)
Percent Error = {%upsilon_{standard} - %upsilon_{calculated}} over { %upsilon_{standard} } * 100	(eqn 3)
All ε in με. Poisson’s Ratio is υ and is unitless.

# II) Data Summary
	Longitudinal (με)	Lateral (με)
Undeflected	0	-222
Deflected	1610	-722
Net Strain	1610	-500

III)	Calculations (25 pts)

Tables and figures should include titles, numbers, and name and units of the presented quantities.
IV)	Comparison and Discussion (25 pts)
The calculated data should be compared with the corresponding theoretical values or values from handbooks (for instance the material properties) in this section. Differences between the theoretical or actual values and your calculated values should be discussed. Include the possible sources of error and how that might have affected the resulting data. When working in your laboratory group, it is recommended to discuss the sources of error with the entire group before the experiment is over. The standard (published) values used in the various experiments are primarily from www.Matweb.com and are given in Table 1.
Table 1: Standard material properties [2]
Material	Material Properties	Used in Laboratories:
Aluminum / (2024-T6)	E = 10.4x106 psi / ν = 0.31	2, 3, and 4
Aluminum / (6061-T651)	E = 10 Msi / σy = 40 ksi / σu = 45 ksi / σb : no standard value / G = 3770 ksi / τprop = 22 ksi	5 and 7
Steel / (1018)	E = 29.7 Msi / σy = 53.7 ksi / σu = 63.8 ksi / σb : no standard value / G = 11.6 Msi / τprop = 31 ksi	5 and 7
Steel (unspecified)	E = 30x106 psi	6 and 8

Units should always be consistent. If it is necessary to look up a reference value, make certain it is in the same system of units as the rest of the values. Do not mix metric and English units. Note that GPa= {10} ^ {9} {N} over {{m} ^ {2}} ≠psi .
You should include your judgement regarding whether the results you obtained are acceptable considering statistical variation and uncertainly analysis. Final conclusions about your results must be presented. Any suggestions regarding the possible improvements of the experiment may also be stated.
# V) References and Appendix (5 points)
# Any references used in the report preparation are to be listed. The laboratory manual should always be mentioned as one of the references. The full title of the references along with other necessary information such as the author(s), publication date, edition number, etc. should be presented. If websites are accessed, the date accessed should be included.
Gilbert, J. A., Carmen, C. L., Thota, J., MAE/CE 370 - MECHANICS OF MATERIALS - LABORATORY MANUAL, Version 3.0, (2015)

MatWeb, http://www.matweb.com, accessed: 8/31/2016.

All your raw notes are included in the Appendix. Attach the actual notes that you recorded while performing the experiment.
The handwritten data sheets recorded during the experiment must be attached. If it is necessary to submit an electronic copy of the report, the raw notes should be scanned or photographed and included in the document.
Appendix A: Units and conversions
Property	English unit(s)	Metric unit(s)
Width, thickness, length, deflection	in, ft	m, cm, mm
Angle	°, radians	°, radians
Percent error	%	%
Area	in2, ft2	m2, cm2, mm2
Moment of Inertia	in4, ft4	m4, cm4, mm4
Force, Load, Weight	lb	N
Torque	in-lb, lb-in	N-m
Stress (normal, shear)	lb/in2 (psi)	N/m2 (Pa)
Modulus of Elasticity / a.k.a. Young’s Modulus E	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Modulus of Rigidity / a.k.a. Shear Modulus G	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Poisson’s Ratio ν	unitless	unitless
Stress Concentration Factor K	unitless	unitless
Strain (normal, shear)	in/in, µε / µε=10-6 in/in	m/m, µε / µε=10-6 m/m

1 ksi	1000 psi
1 in	25.4 mm
1 lb	4.448 N, 453.6 g