# MAE 370 laboratory section (9)
# Laboratory (5): Beam Deflection
# Experiment conducted: (2016-10-14)
# Report submitted: (2016-10-21)
# Author:
Cory Wolfe
Group: C

# I) Procedure
The general setup for this lab involved mounting a beam on two supports and placing an array of gages on the beam that measured the displacement of the beam. After the beam was mounted and the hangers for the holding the weights were mounted the initial gages were placed in the appropriate location and zeroed out. A rough sketch of the beam is shown at the bottom of this section. The procdures discussed here come from section 11.4 of the provided MAE 370 Lab Manual.
The group then placed the weights on in the appropriate increments while recording the deflection on the beam. Due to the number of gages the group had to run the experiment multiple times with the gages placed at different increments on the beam. The group made use of a steel beam, the mounting harness, the gages, a series of weights and hangers to mount the weights to the beam.
Items used:
- Beam
- Weights
- Hanger
- Deflection gages
- Mounting device
EIy = { P*x^3 } over { 12 } - { PL^2 x } over { 16 }, 0<=x<={ L }over { 2 }	(eqn 1)
EIy = { -P*x^3 } over { 12 } + { PLx^2 } over { 4 } - {3PL^2 x} over {16}+{PL^3}over{48}, { L }over { 2 }<=x<=L	(eqn 2)
EIy = { Px^3 }over{ GL }( a-b ) -{ Pax^2 }over{ 2 } + { PL} over{6 }( 2a+b)x, 0<=x<=L	(eqn 3)
Equations 1 and 2 for conditions with central load, equation 3 is for the overhanging load.
E in psi
I in in4
P in lb
x, L, y, a, b in in
Schematics:

# II) Data Summary
Central:
Step	Load(lb)	Gage 1	Gage 2	Gage 3	Gage 4
1	1	.007	.014	.013	.007
2	2	.014	.026	.025	.014
3	3	.022	.040	.038	.021
4	4	.030	.052	.051	.027
5	5	.037	.066	.063	.034

Dial Gages (in):
x1	5
x2	10
x3	20
x4	25

Overhanging:
Step	Load(lb)	Gage 1	Gage 2	Gage 3
1	1	.012	.015	.011
2	2	.022	.030	.022
3	3	.033	.045	.034
4	4	.045	.060	.045
5	5	.056	.075	.057

Dial Gages (in):
x1	7.5
x2	15
x3	22.5

Beam Dimensions (in):
L	30
w	1
t	.25
a	5
b	5

III)	Calculations (25 pts)

Most of the calculations for this lab were performed in a separate excel sheet that is attached. In this Calculations section there is a plot of deflections and table of data from the overhanging load's data and calculations, to show the calculated data. Further information regarding this is found in the excel document that accompanies this report.

IV)	Comparison and Discussion (25 pts)
Overall, and in all specific cases the data is acceptable in comparison to the theoretical values calculated. The worst error was a over twelve percent at 10 inches into the beam for the 1 pound central load. The gage reading was .014 and the theoretical value was .0124. There is a possibility that the error would have been lowered if the gage returned more signifigant figures.
Some possible sources of error include poor measurements with a tape measure, in addition to movement of the hanger and beam while the group moved gages and added weights. Overall these sources of error did not show a major effect on the groups result, as the average error was less than 4 percent overall.
Table 1: Standard material properties [2]
Material	Material Properties	Used in Laboratories:
Aluminum / (2024-T6)	E = 10.4x106 psi / ν = 0.31	2, 3, and 4
Aluminum / (6061-T651)	E = 10 Msi / σy = 40 ksi / σu = 45 ksi / σb : no standard value / G = 3770 ksi / τprop = 22 ksi	5 and 7
Steel / (1018)	E = 29.7 Msi / σy = 53.7 ksi / σu = 63.8 ksi / σb : no standard value / G = 11.6 Msi / τprop = 31 ksi	5 and 7
Steel (unspecified)	E = 30x106 psi	6 and 8

# V) References and Appendix (5 points)
Gilbert, J. A., Carmen, C. L., Thota, J., MAE/CE 370 - MECHANICS OF MATERIALS - LABORATORY MANUAL, Version 3.0, (2015)

1. MatWeb, http://www.matweb.com, accessed: 8/31/2016.
2. Attached data for Fixed-Fixed test, received from TA.
Appendix A: Units and conversions
Property	English unit(s)	Metric unit(s)
Width, thickness, length, deflection	in, ft	m, cm, mm
Angle	°, radians	°, radians
Percent error	%	%
Area	in2, ft2	m2, cm2, mm2
Moment of Inertia	in4, ft4	m4, cm4, mm4
Force, Load, Weight	lb	N
Torque	in-lb, lb-in	N-m
Stress (normal, shear)	lb/in2 (psi)	N/m2 (Pa)
Modulus of Elasticity / a.k.a. Young’s Modulus E	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Modulus of Rigidity / a.k.a. Shear Modulus G	lb/in2 (psi) / Msi=106 psi	N/m2 (Pa) / GPa=109 Pa
Poisson’s Ratio ν	unitless	unitless
Stress Concentration Factor K	unitless	unitless
Strain (normal, shear)	in/in, µε / µε=10-6 in/in	m/m, µε / µε=10-6 m/m

1 ksi	1000 psi
1 in	25.4 mm
1 lb	4.448 N, 453.6 g